## Slide 1: Switching Features and Technologies for the Campus Network
CCNP SWITCH: Implementing Cisco IP Switched Networks

## Slide 2: Chapter 8 Objectives
This chapter covers the following Cisco Catalyst switch features:
Discovery protocols
Unidirectional Link Detection
Power over Ethernet
SDM templates
Monitoring features
IP SLA
Notes: Chapter 1 Objectives

## Slide 3: Discovery Protocols
This section on discovery protocols covers the following topics:
Introduction to LLDP and comparison to CDP
Basic configuration of LLDP
Discovering neighbors using LLDP

## Slide 4: Introduction to LLDP
LLDP is an industry standard protocol for neighbor discovery.
All current Cisco devices support LLDP, and only legacy and end-of-sale platforms may not support LLDP.
Notes: Because of the industry standard requirements around network designs, many campus networks are now leveraging LLDP over CDP.
By definition, LLDP is a neighbor discovery protocol that is used for network devices to advertise information about themselves to other devices on the network.
This protocol runs over the data link layer, which allows two systems running different network layer protocols to learn about each other.
LLDP is locally significant, and the switch does not forward LLDP information; the switch only processes the information.

## Slide 5: Introduction to LLDP
This protocol can advertise details such as configuration information, device capabilities, IP address, hostname, and device identity.
LLDP is used for a plethora of information sharing, it is not architected to send out real-time information such as performance data or counter data.
An advantage of LLDP over CDP is that it allows for customization. LLDP can carry a lot of information that is relevant to your network.
One drawback of LLDP in comparison to CDP is that it is not very lightweight.

## Slide 6: Introduction to LLDP
The following list captures a few important implementation properties of LLDP:
LLDP is unidirectional.
LLDP operates only in an advertising mode.
LLDP does not solicit for information or monitor state changes between LLDP nodes.
LLDP leverages a Layer 2 multicast frame to notify neighbors of itself and its properties.
LLDP will receive and record all information it receives about its neighbors.
LLDP uses 01:80:c2:00:00:0e, 01:80:c2:00:00:03, or 01:80:c2:00:00:00 as the destination multicast MAC address.

## Slide 7: Introduction to LLDP
The following list defines the most common information exchanged with LLDP with campus switches:
System name and description
Port name and description
Port VLAN and VLAN name
Management IP address
System Capabilities (Wi-Fi, routing, switching, and so on)
Power over Ethernet
Link aggregation

## Slide 8: Basic Configuration of LLDP
CDP is enabled by default on all Cisco devices, but LLDP may be either enabled or disabled by default, depending on the hardware platform and software version.
Therefore, to enable LLDP on a device, use the command lldp run in global configuration mode. To disable it, use no lldp run.
To disable LLDP on a specific interface, you need to disable both LLDP from receiving or transmitting LLDP by issuing both the no lldp receive and no lldp transmit commands.
Notes: Note Because LLDP is enabled by default on select platforms and software versions, the lldp receive and lldp transmit commands will not appear in the configuration by default.

## Slide 9: Basic Configuration of LLDP

## Slide 10: LLDP Neighbors

## Slide 11: LLDP Traffic Info

## Slide 12: LLDP Key Features
LLDP allows network management applications to automatically discover and learn about network devices.
LLDP is the industry standard alternative to the CDP.
LLDP supports enabling or disabling either transmitting or receiving capabilities per port.
To view LLDP neighbors, use the show lldp neighbors [ detail ] command.

## Slide 13: Power over Ethernet
Power over Ethernet (PoE) supplies power through the same cable as data.

## Slide 14: PoE benefits
PoE switches support remote management where power adapters and injectors do not.
PoE switches allow for centralized methods of backup power.
PoE requires less configuration than a local power adapter or injector.
PoE leverages the data cabling infrastructure, and no additional power cable is required as with the case with power adapters or injectors.
Notes: Note Cisco highly recommends leveraging alternate and backup power sources when deploying PoE such as an uninterruptible backup supply (UPS) backup, generator power, and so on. Without backup power in the case of a power failure, Cisco IP phones will cease to function.

## Slide 15: PoE Components
PoE terminology refers to three types of components:
Power-sourcing devices
  Cisco Catalyst switches and power injectors
Powered devices
  Access points, IP phones, and IP cameras.
  Thin clients, sensors, wall clocks, and so on.
  Even switches can be powered through PoE itself.
Ethernet cabling.
  As with standard Ethernet, the distance of PoE is limited to 100 meters with Category 5 cabling.

## Slide 16: PoE Standards
IEEE 802.3af (ratified 2003)
  This standard provides interoperability between different vendors.
  Up to 15.4 W of DC power is available for each powered device.
IEEE 802.3at (ratified 2009)
  This standard is an improvement over the 802.3af standard, and can provide powered devices with up to 25.5 W of power.
  This number can be increased to 50 W and more with implementations that are outside the standard.
  This standard is also known as PoE+ or PoE Plus.
Notes: Because Cisco generally leads in technologies before standards are available, Cisco originally only supported the prestandard Cisco Inline Power standard (circa 2000).
Eventually, standards committees released an IEEE standards-based power specification and more recently updated this power specification.

## Slide 17: PoE Negotiation
The Cisco switches do not supply power to a port unless it specifically detects the need by the end device.
This prevents wasting of unnecessary power and so on.
With 802.3af and 802.3at, the switch tries to detect the powered device by supplying a small voltage across the Ethernet cable.
The switch then measures the resistance. If the measured resistance is 25K ohm, a powered device is present.
The powered device can provide the switch with a power class information.
The default class of 0 is used if either the switch or the powered device does not support power class discovery

## Slide 18: PoE Power Classes
Notes: Note The original Cisco Inline Power method has a different method of negotiating power than both of the IEEE standards. The switch sends out a 340-kHz test tone on the Ethernet cable. A tone is transmitted instead of DC power because the switch must first detect the device before supplying it with power. The most appropriate power level is then determined by exchange of CDP information. The switch discovers the type of device (for example, a Cisco IP phone) and the power requirements of the device.

## Slide 19: Configuring and Verifying PoE

## Slide 20: SDM Templates
Upon completing this section on SDM templates, you will be able to do the following:
Describe the typical SDM template types
Change the SDM template
Describe precautions to take when changing the SDM templates
Notes: The Switching Database Manager (SDM) templates on specific access layer switches (such as Cisco Catalyst 2960, 3560, or 3750) manages how Layer 2 and Layer 3 switching information is maintained in the ternary content-addressable memory (TCAM). So, different Cisco SDM templates are used for optimal use of system resources for specific features or feature set combination. Although the default SDM is configured for optimal use of all features simultaneously, SDM may be tweaked for those corner-case or specific scenarios.
As an example, the most common SDM default modification action is when deploying a combination of both IPv4 and IPv6 (dual stack) because IPv6 functionality is not supported with the default template.

## Slide 21: SDM Template Types
SDM templates modify system resources such as CAM and TCAM.
SDM templates:
Default
  The default template; this template provides for a mix of unicast routes, connected, and host routes.
Routing
  As one example, you would enable this template if the device is performing routing in the distribution or core of the network. The device is able to carry numerous routes, but only for IPv4.
Access
  You would enable this template if you have many VLANs. In turn, this template reduces the resources that are allocated to routing.

## Slide 22: SDM Template Types
VLAN
  When you enable this template, you allocate most of the table space to Layer 2 unicasts. You would use this when you have large subnets with many MAC addresses.
Dual IPv4 and IPv6
  You would enable this template if you want to turn on the IPv6 capabilities of the device. When enabling this template, you have to choose between default, routing, and VLAN:
  Default
    More space is reserved for IPv6 routing and security. There is less reserved space for Layer 2 unicast.
  Routing
    More space is reserved for IPv6 routing than IPv4 routing.
  VLAN
    Suitable for when you are running a dual-stack environment with lots of VLANs.

## Slide 23: Choosing the Right SDM Template
It is a best practice to change the SDM template only if you have a good reason to do so.
Before changing the template, investigate whether the change is needed or if it is just a workaround for poor design choices.
As another best practice, always investigate the amount of systems resources being used prior to considering changes to the SDM template.
To verify how much of the system resources are being used, use the command show platform tcam utilization .
If the TCAM utilization is close to maximum for any of the parameters, check if any of the other template features can optimize for that parameter:
  show sdm prefer { access | default | dual-ipv4-and-ipv6 | routing | vlan }.
Another common reason for changing the SDM template is because you are running out of a specific resource.
  For example, the use of the switch in a large Layer 2 domain with many ACLs may require a change to the access SDM template.

## Slide 24: System Resource Configuration on Other Platforms
SDM templates configure the switch for specific allocation of finite resources.
The use of SDM templates is summarized as follows:
To verify the amount of resources being used, use the command show platform tcam utilization.
To verify the SDM template that is currently in use, use the command show sdm prefer.
To change the template to dual stack, use the command sdm prefer dual-ipv4-and-ipv6 default.
  When changing the SDM template, a reload of the switch is required.
Notes: The concept of SDM templates is applicable to Cisco Catalyst 3750 and other platforms; specific Catalyst platforms such as the Catalyst 6500 that do not use SDM templates have a similar method to adjust allocation of finite resources.

## Slide 25: Displaying SDM Resources

## Slide 26: Displaying SDM Resources

## Slide 27: Monitoring Features
Upon completing this lesson, you will be able to meet these objectives:
Describe SPAN
Describe SPAN terminology
Describe different versions of SPAN
Configure SPAN
Verify local SPAN configuration
Configure RSPAN
Verify RSPAN configuration
Notes: Because switches do not flood traffic on all ports, use of the Switch Port Analyzer (SPAN) feature is necessary to ensure appropriate traffic is fed to these traffic sniffers.

## Slide 28: SPAN and RSPAN Overview
SPAN session: An association of a destination port with source ports.
Source VLAN: VLAN monitored for traffic analysis.

## Slide 29: SPAN Terminology

## Slide 30: Remote SPAN Overview
Remote SPAN supports source and destination ports on different switches, while local SPAN supports only source and destination ports on the same switch.

## Slide 31: RSPAN
In terms of configuration, RSPAN consists of the following:
RSPAN source session
RSPAN VLAN
RSPAN destination session
Notes: Your monitored traffic is flooded into RSPAN VLAN that is dedicated for the RSPAN session in all participating switches. RSPAN destination port can then be anywhere in that VLAN.

## Slide 32: SPAN Configuration
SPAN adheres to the following caveats
A destination port cannot be a source port or vice versa.
The number of destination ports is platform dependent; some platforms allow for more than one destination.
Destination ports do not act as normal ports and do not participate in spanning tree and so on. Normal traffic flows through a destination. Be careful not to connect anything besides an end device to a SPAN destination port.

## Slide 33: SPAN Configuration

## Slide 34: RSPAN Configuration
SW1(config)# vlan 100
SW1(config-vlan)# name RSPAN-VLAN
SW1(config-vlan)# remote-span
SW1(config-vlan)# exit
SW1(config)# monitor session 2 source interface Giga0/1
SW1(config)# monitor session 2 destination remote vlan 100

## Slide 35: RSPAN Configuration
SW2(config)# vlan 100
SW2(config-vlan)# name RSPAN-VLAN
SW2(config-vlan)# remote-span
SW2(config-vlan)# exit
SW2(config)# monitor session 2 destination interface Giga 0/2
SW2(config)# monitor session 2 source remote vlan 100

## Slide 36: RSPAN Verification

## Slide 37: Local SPAN
Span source
  One or more ports
    Can be in same or different vlans
  Entire VLAN (VSPAN)
  Trunk ports can
    Can use a vlan filter on span source to limit traffic to certain vlans
  Etherchannel/Portchannel
    Individual ports that are members or etherchannel as well
      Only sees the traffic on that physical member
Pg 353

## Slide 38: Local SPAN
Span destination for a local span is on the same switch
If the bandwidth of SPAN source traffic exceeds that of the SPAN destination port, some mirrored traffic might not be seen at the destination port
Drops from the back of the transmit queue of the destination port
Pg 354

## Slide 39: SPAN Destination
SPAN normally copies packets to the destination without any VLAN trunk tags
SPAN usually ignores switch generated control packets
  Spanning Tree Protocol (STP) bridge protocol data units (BPDUs)
  Cisco Discovery Protocol (CDP), Virtual Trunking Protocol (VTP)
  Dynamic Trunking
  Protocol (DTP)
  Page Aggregation Protocol (PAgP)
Can capture control protocols with encapsulate replicate
Pg 355

## Slide 40: SPAN Destination
SPAN destination interface only transmits mirrored traffic by default.
If you connect a device that also needs to transmit data back into the network, you can override the default SPAN behavior.
Add the following command syntax to the monitor session destination command to allow ingress traffic:
ingress { dot1q vlan vlan-id | isl | untagged vlan vlan-id }
If SPAN source is a trunk, you can limit the mirrored traffic to only certain VLANS
Switch(config)# monitor session session-number filter vlan vlan-range
Pg 355

## Slide 41: Remote SPAN
If the analyzer can’t be placed locally, use a remote span
With RSPAN, the source and destination can be located on different switches in different locations.
The RSPAN source is identified on one switch where the source is connected, just as with local SPAN.
The RSPAN destination is identified on another switch where the mirrored traffic will be collected.
Then RSPAN will carry only the mirrored data over a special purpose VLAN across trunk links and intermediate switches between the source and destination.
  As long as every switch along the way is RSPAN capable
Pg 356

## Slide 42: Remote SPAN
The RSPAN VLAN has some important differences from a regular VLAN.
  MAC address learning is disabled on the RSPAN VLAN.
An RSPAN-capable switch also floods the RSPAN packets out all its ports belonging to the RSPAN VLAN
Make sure only the transport ports are in the RSPAN vlan
Pg 356

## Slide 43: IP SLA
Upon completion of this section, you will understand the following:
Basic use cases of IP SLA
What an IP SLA source and responder are
Basic example of an ICMP IP SLA configuration and a UDP configuration

## Slide 44: Introduction to IP SLA
An SLA (service level agreement) is a contract between the network provider and its customers, or between a network department and internal corporate customers. It provides a form of guarantee to customers about the level of user experience.
SLA may contain specifics about connectivity and performance agreements for an enduser service from a service provider.
An SLA typically outlines the minimum level of service and the expected level of service.
Notes: The networking department can use the SLAs to verify that the service provider is meeting its own SLAs or to define service levels for critical business applications.
Typically, the technical components of an SLA contain a guaranteed level for network availability, network performance in terms of round-trip-time (RTT), and network response in terms of latency, jitter, and packet loss. The specifics of an SLA vary depending on the applications that an organization is supporting in the network.

## Slide 45: Introduction to IP SLA
An SLA can also be used as the basis for planning budgets and justifying network expenditures.
Overall, the IP SLA feature provides real-time feedback about network reachability. For features such as voice and video, network availability with stable jitter and latency are important.
The IP SLA provides the feedback necessary to ensure the network can sustain real-time applications as well as mission-critical applications such as web portal or ordering.

## Slide 46: IP SLA Additional Uses
Additional functions and uses for IP SLA are as follows:
Edge-to-edge network availability monitoring.
Network performance monitoring and network performance visibility
Voice over IP (VoIP), video, and virtual private network (VPN) monitoring
SLA monitoring
IP service network health
MPLS network monitoring
Troubleshooting of network operation

## Slide 47: IP SLA Options
Switch(config-ip-sla)# ?
IP SLAs entry configuration commands:
dhcp DHCP Operation
dns DNS Query Operation
exit Exit Operation Configuration
ftp FTP Operation
http HTTP Operation
icmp-echo ICMP Echo Operation
path-echo Path Discovered ICMP Echo Operation
path-jitter Path Discovered ICMP Jitter Operation
tcp-connect TCP Connect Operation
udp-echo UDP Echo Operation
udp-jitter UDP Jitter Operation

## Slide 48: IP SLA Source and Responder
The source is the Cisco IOS device that sends probe packets.
The destination of the probe may be another Cisco device or another network target such as a web server or IP host.
Although the destination of the majority of the tests can be any IP device, the measurement accuracy of some of the tests can be improved with an IP SLA responder.
An IP SLA responder is a device that runs Cisco IOS Software.
The responder adds a time stamp to the packets sent so the IP SLA source can take into account any latency that occurred while the responder is processing the test packets.
For this test to work properly, both the source and responder clocks need to be synchronized through Network Time Protocol (NTP).

## Slide 49: IP SLA Configuration
To implement IP SLA network performance measurement, you need to perform the following tasks:
Step 1. Enable the IP SLAs responder, if required.
Step 2. Configure the required IP SLA’s operation type.
Step 3. Configure any options available for the specified operation type.
Step 4. Configure threshold conditions, if required.
Step 5. Schedule the operation to run, and then let the operation run for a period of time to gather statistics.
Step 6. Display and interpret the results of the operation using the Cisco IOS CLI or a network management system (NMS) with SNMP.

## Slide 50: IP SLA ICMP Echo Confi guration Example
Notes: The ip sla operation-number command creates the IP SLA instance and enters the IP SLA configuration mode. The icmp-echo command has many options. The full command syntax is as follows: icmp-echo { destination-ip-address | destination-hostname } [ source-ip { ip-address | hostname } | source-interface interface-id ]. In Example 8-9 , the destination IP address is explicitly defined; however, the command does support hostnames and sourcing the echo from specific IP addresses or interfaces. The command has a default of 60 seconds and configures the rate at which IP SLAs are repeated. In this case, the echoes will occur every 30 seconds.
The ip sla schedule global schedule command controls the scheduling parameters of the individual IP SLA operation. The full syntax of the command is as follows: ip sla schedule operation-number [ life { forever | seconds }] [ start-time { hh : mm [: ss ] [ month day | day month ] | pending | now | after hh:mm:ss ] [ ageout seconds ] [ recurring ]. In Example 8-8 , the IP SLA will start immediately after the command is issued and will run forever . As indicated in the command options, IP SLA supports specific start times, end times, age out, and reoccurrence.

## Slide 51: Verify IP SLA Configuration

## Slide 52: Verify IP SLA Configuration

## Slide 53: IP SLA Operation with Responder
Notes: 1. At the start of the control phase, the IP SLA source sends a control message with the configured IP SLA operation information to IP SLA control port UDP 1967 on the target router. The control message carries information such as protocol, port number, and duration.
  If MD5 authentication is enabled, message digest 5 (MD5) algorithm checksum is sent with the control message.
  If the authentication of the message is enabled, the responder verifies it; if the authentication fails, the responder returns an authentication failure message.
  If the IP SLA measurement operation does not receive a response from a responder, it tries to retransmit the control message and eventually times out.
2. If the responder processes the control message, it sends an OK message to the source router and listens on the port that is specified in the control message for a specified duration. If the responder cannot process the control message, it returns an error. In the figure, UDP port 2020 is used for the IP SLA test packets.
3. If the return code of the control message is OK, the IP SLA operation moves to the probing phase, where it will send one or more test packets to the responder for response time computations. The return code is available with the show ip sla statistics command. In Figure 8-9 , these test messages are sent on control port 2020.
4. The responder accepts the test packets and responds. Based on the type of operation, the responder may add an “in” time stamp and an “out” time stamp in the response packet payload to account for CPU time that is spent in measuring unidirectional packet loss, latency, and jitter to a Cisco device. These time stamps help the IP SLA source to make accurate assessments on one-way delay and the processing time in the target routers. The responder disables the user-specified port after it responds to the IP SLA measurements packet or when a specified time Expires.

## Slide 54: IP SLA Time Stamps
T1 time is marked from 0 in milliseconds for simplicity.
The RTT in this example is calculated as
RTT = T5 – (T5-T4) - (T3-T2) = 1.5msec – (1.5msec-1.3msec) – (0.7msec - 0.5msec) = 1.1msec .

## Slide 55: Configuring Authentication for IP SLA

## Slide 56: IP SLA UDP Jitter Example
Notes: Switch(config-ip-sla)# udp-jitter dest-ip-add dest-udp-port [ source-ip src-ip-add ] [ source-port src-udp-port] [ num-packets num-of-packets ] [ interval packet-interval ]
request-data-size 160 (syze in bytes - payload)

## Slide 57: Chapter 8 Summary
LLDP and the legacy CDP features are useful for discovering neighbor adjacencies and their details.
The UDLD aggressive mode feature is useful in adding resiliency to networks to avoid disasters in case of anomalous behaviors.
SPAN and RSPAN are common debugging and traffic capture features that are also leveraged to capture traffic for network analytics.
The IP SLA