## Slide 1: Network Protocols and Services
Instructor Materials
CCNA Cybersecurity Operations v1.0
Notes: Cisco Networking Academy Program
CCNA Cybersecurity Operations v1.1
Chapter 4: Network Protocols and Services

## Slide 2: Network Protocols
Notes: 4 – Network Protocols and Services
4.1 – Network Protocols

## Slide 3: Network Communications Process Views of the Network
Views of the network
  Small home network
  SOHO (Small Office/Home Office)
  Medium to large networks
  World-wide networks
Notes: 4.1 – Network Protocols
4.1.1 – Network Communications Process
4.1.1.1 – Views of the Network

## Slide 4: Network Communications Process Client-Server Communications
File Client and Server communications
  Server stores corporate and user files.
  Client devices access these files or services with client software.
Web Client Server
  Web Server runs web server software and client uses browser software.
Email Client-Server communications
  Email Server runs email server software.
Notes: 4.1 – Network Protocols
4.1.1 – Network Communications Process
4.1.1.2 – Client – Server Communications

## Slide 5: Network Communications Process A Typical Session: Student
A Typical Session: Student
  Determine the origin of the traffic enter the network.
  For example, Terry’s data flows with the data of thousands of other users along a fiber-optic network that connects Terry’s ISP with the several other ISPs, including the ISP that is used by the search engine company. Eventually, Terry’s search string enters the search engine company’s website and is processed by its powerful servers. The results are then encoded and addressed to Terry’s school and her device.
Notes: 4.1 – Network Protocols
4.1.1 – Network Communications Process
4.1.1.3 – A typical session: student

## Slide 6: Network Communications Process A Typical Session: Gamer
A Typical Session: Gamer
  Determine the origin of the traffic enter the network.
  Michelle’s network, like many home networks, connects to an ISP using a router and modem. These devices allow Michelle’s home network to connect to a cable TV network that belongs to Michelle’s ISP. The cable wires for Michelle’s neighborhood all connect to a central point on a telephone pole and then connect to a fiber-optic network. This fiber-optic network connects many neighborhoods that are served by Michelle’s ISP.
Notes: 4.1 – Network Protocols
4.1.1 – Network Communications Process
4.1.1.4 – A typical session: gamer

## Slide 7: Network Communications Process A Typical Session: Surgeon
A Typical Session: Surgeon
  Determine the origin of the traffic enter the network
  Dr. Ismael Awad is an oncologist who performs surgery on cancer patients. He frequently needs to consult with radiologists and other specialists on patient cases. The hospital that Dr. Awad works for subscribes to a special service called a cloud. The cloud allows medical data, including patient x-rays and MRIs to be stored in a central location that is accessed over the Internet.
Notes: 4.1 – Network Protocols
4.1.1 – Network Communications Process
4.1.1.5 – A typical session: surgeon

## Slide 8: Network Communications Process Tracing the Path
Cybersecurity analysts must be able to determine the origin of traffic that enters the network, and the destination of traffic that leaves it. Understanding the path that network traffic takes is essential to this.
Tier 1 Network and Tier 2 networks usually connect through an Internet Exchange Point (IXP).
Larger networks connect to Tier 2 networks, usually through a Point of Presence (POP).
Tier 3 ISPs connect homes and businesses to the Internet.
Notes: 4.1 – Network Protocols
4.1.1 – Network Communications Process
4.1.1.6 – Tracing the Path

## Slide 9: Communications Protocols What are Protocols?
Protocol – The rules of communications
  Network protocols provide the means for computers to communicate on networks.
  Network protocols dictate the message encoding, formatting, encapsulation, size, timing, and delivery options.
Notes: 4.1 – Network Protocols
4.1.2 – Communications Protocols
4.1.2.1 – What are Protocols?

## Slide 10: Communications Protocols Network Protocol Suites
  Describe precise requirements and interactions.
  Define a common format and set of rules for exchanging messages between devices.
  Some common networking protocols are Hypertext Transfer Protocol (HTTP), Transmission Control Protocol (TCP), and Internet Protocol (IP).
Notes: 4.1 – Network Protocols
4.1.2 – Communications Protocols
4.1.2.2 – Network Protocol Suites

## Slide 11: Communications Protocols TCP/IP Protocol Suite
TCP/IP has standardized the way the computers communicate.
TCP/IP protocols are specific to the application, transport, Internet, and network access layers.
TCP/IP protocol suite is implemented on both the sending and receiving hosts to provide end-to-end delivery of messages over a network.
Notes: 4.1 – Network Protocols
4.1.2 – Communications Protocols
4.1.2.3 – TCP/IP Protocol Suites

## Slide 12: Communications Protocols Format, Size, and Timing
Format
  Encapsulation - process of placing one message format inside another message format.
  Decapsulation - the reverse process of encapsulation.
Size – Message is broken up into many frames when sent, and reconstructed into the original message when received.
Timing – includes the access method, flow control, and response timeout.
Notes: 4.1 – Network Protocols
4.1.2 – Communications Protocols
4.1.2.4 – Format, Size, and Timing

## Slide 13: Communications Protocols Unicast, Multicast, and Broadcast
Unicast – one-to-one
Multicast – one-to-many
Broadcast – one-to-all
Notes: 4.1 – Network Protocols
4.1.2 – Communications Protocols
4.1.2.5 – Unicast, Multicast, and Broadcast

## Slide 14: Communications Protocols Reference Models
Notes: 4.1 – Network Protocols
4.1.2 – Communications Protocols
4.1.2.6 – Reference Models

## Slide 15: Communications Protocols Three Addresses
Three important addresses:
  Protocol address
  Network host address
  Physical address
  Addressing is used by the client to send requests and other data to a server. The server uses the client’s address to return the requested data to the client that requested it.
Notes: 4.1 – Network Protocols
4.1.2 – Communications Protocols
4.1.2.7 – Three Addresses

## Slide 16: Communication Protocols Encapsulation
This division of data into smaller pieces is called segmentation. Segmenting messages has two primary benefits:
  Segmentation
  Multiplexing
The application data is encapsulated with various protocol information as it is passed down the protocol stack.
The form that an encapsulated piece of data takes at any layer is called a protocol data unit (PDU).
Notes: 4.1 – Network Protocols
4.1.2 – Communications Protocols
4.1.2.8 – Encapsulation

## Slide 17: Communication Protocols Encapsulation (Cont.)
This process is reversed at the receiving host, and is known as de-encapsulation. The data is de-encapsulated as it moves up the stack toward the end-user application.
Notes: 4.1 – Network Protocols
4.1.2 – Communications Protocols
4.1.2.8 – Encapsulation

## Slide 18: Communications Protocols Scenario: Sending and Receiving a Web Page
HTTP – This application protocol governs the way a web server and a web client interact.
TCP – This transport protocol manages individual conversations. TCP divides the HTTP messages into smaller pieces, called segments. TCP is also responsible for controlling the size and rate at which messages are exchanged between the server and the client.
IP – This is responsible for taking the formatted segments from TCP, encapsulating them into packets, assigning them the appropriate addresses, and delivering them to the destination host.
Ethernet – This network access protocol is responsible for taking the packets from IP and formatting them to be transmitted over the media.
Notes: 4.1 – Network Protocols
4.1.2 – Communications Protocols
4.1.2.9 – Scenario: Sending and Receiving a Web Page

## Slide 19: Ethernet and Internet Protocol (IP)
Notes: 4 – Network Protocols and Services
4.2 – Ethernet and Internet Protocol (IP)

## Slide 20: Ethernet The Ethernet Protocol
Operates at Layer 1 and 2
  Defined by the IEEE 802.2 and 802.3 standards
  Ethernet Sublayers
    Logical Link Layer (LLC)
    Media Access Control Layer (MAC)
Ethernet responsibilities
  Data encapsulation
  Media access control
Notes: 4.2 – Ethernet and Internet Protocol (IP)
4.2.1 – Ethernet
4.2.1.1 – The Ethernet Protocol

## Slide 21: Ethernet The Ethernet Frame
Minimum Ethernet frame size 64 bytes
Maximum Ethernet frame size 1518 bytes
Two key identifiers
  Destination MAC address
  Source MAC address
Uses hexadecimal
Notes: 4.2 – Ethernet and Internet Protocol (IP)
4.2.1 – Ethernet
4.2.1.2 – The Ethernet Frame

## Slide 22: Ethernet MAC Address Format
Ethernet MAC address is 48-bit binary expressed as 12 hexadecimal digits.
  Uses numbers 0 to 9 and letters A to F.
  All data that travels on the network is encapsulated in Ethernet frames.
Notes: 4.2 – Ethernet and Internet Protocol (IP)
4.2.1 – Ethernet
4.2.1.3 – MAC Address Format
4.2.1.4 – Activity- Ethernet Frame Fields

## Slide 23: IPv4 IPv4 Encapsulation
IP encapsulates the transport layer segment by adding an IP header.
Notes: 4.2 – Ethernet and Internet Protocol (IP)
4.2.2 – IPv4
4.2.2.1 – IPv4 Encapsulation

## Slide 24: IPv4 IPv4 Characteristics
IPv4 Characteristics
Connectionless – no dedicated end-to-end connection is created before data is sent.
Unreliable (Best Effort) - IP protocol does not guarantee that all packets that are delivered are, in fact, received.
Media Independent - IP operates independently of the media that carry the data at lower layers of the protocol stack.
Notes: 4.2 – Ethernet and Internet Protocol (IP)
4.2.2 – IPv4
4.2.2.2 – IPv4 Characteristics
4.2.2.3- Activity – IPv4 Characteristics

## Slide 25: IPv4 IPv4 Packet
Packet header consists of fields containing important information about the packet.
Fields contain binary numbers examined by the Layer 3 process.
The binary values of each field identify various settings of the IP packet.
Two most commonly referenced fields are the source and destination IP addresses.
Notes: 4.2 – Ethernet and Internet Protocol (IP)
4.2.2 – IPv4
4.2.2.4- IPv4 Packet

## Slide 26: IPV4 Addressing Basics IPv4 Host Address Structure
IPv4 address is a hierarchical address that is made up of a network portion and a host portion.
The network portion of the address must be identical for all devices that reside in the same network.
The bits within the host portion of the address must be unique to identify a specific host within a network.
Notes: 4.2 – Ethernet and Internet Protocol (IP)
4.2.3 – IPv4 Addressing Basics
4.2.3.1 – IPv4 Host Address Structure

## Slide 27: IPv4 Addressing Basics IPv4 Subnet Mask and Network Address
Subnetting takes a network space and divides it into smaller spaces called subnets.
Identifying network address of an IPv4host:
  IP address is logically ANDed, bit by bit with subnet mask.
  ANDing between the address and the subnet mask yields the network address.
Notes: 4.2 – Ethernet and Internet Protocol (IP)
4.2.3 – IPv4 Addressing Basics
4.2.3.3 – IPv4 Subnet Mask and Network Address

## Slide 28: IPv4 Addressing Basics Subnetting Broadcast Domains
Subnetting takes a network space and divides it into smaller spaces called subnets.
Identifying network address of an IPv4 host:
  IP address is logically ANDed, bit by bit with subnet mask.
  ANDing between the address and the subnet mask yields the network address.
Notes: 4.2 – Ethernet and Internet Protocol (IP)
4.2.3 – IPv4 Addressing Basics
4.2.3.4 – Subnetting Broadcast Domains

## Slide 29: Types of IPv4 Addresses IPv4 Address Classes and Default Subnet Masks
Assigned Classes – A, B, C, D, and E
Class A - Designed to support extremely large networks.
Class B – Designed to support moderate to large networks.
Class C- Designed to support small networks.
Class D - Multicast block.
Class E - Experimental address block.
Notes: 4.2 – Ethernet and Internet Protocol (IP)
4.2.4 – Types of IPv4 Addresses
4.2.4.1 – IPv4 Address Classes and Default Subnet Masks

## Slide 30: Types of IPv4 Addresses Reserved Private Addresses
Blocks of addresses mostly used by organizations to assign IPv4 addresses to internal hosts.
Not unique to any network.
Not allowed on Internet and are filtered by internal router.
Router usually connects the internal network to the ISP network.
Notes: 4.2 – Ethernet and Internet Protocol (IP)
4.2.4 – Types of IPv4 Addresses
4.2.4.2 – Reserved Private Addresses

## Slide 31: The Default Gateway Host Forwarding Decision
A host can send a packet to three types of destinations:
  Itself - A host can ping itself by sending a packet to a special IPv4 address of 127.0.0.1. Pinging the loopback interface tests the TCP/IP protocol stack.
  Local host - This is a host on the same local network.
  Remote host - This is a host on a remote network. The hosts do not share the same network address.
Notes: 4.2 – Ethernet and Internet Protocol (IP)
4.2.5 – The Default Gateway
4.2.5.1 – Host Forwarding Decision

## Slide 32: The Default Gateway Default Gateway
Three dotted decimal IPv4 addresses must be configured when assigning an IPv4 configuration to host:
  IPv4 address – Unique IPv4 address of the host.
  Subnet mask - Used to identify the network/host portion of the IPv4 address.
  Default gateway – Identifies the local gateway (i.e. local router interface IPv4 address) to reach remote networks.
The default gateway is the network device that can route traffic to other networks. It is the router that can route traffic out of the local network.
Notes: 4.2 – Ethernet and Internet Protocol (IP)
4.2.5 – The Default Gateway
4.2.5.2 – Default Gateway

## Slide 33: The Default Gateway Using the Default Gateway
A host's routing table will typically include a default gateway.
The host receives the IPv4 address of the default gateway.
IP addressing information:
  Configured manually.
  Obtained automatically/dynamically using Dynamic Host Configuration Protocol (DHCP).
  Placed in computer’s routing table.
Notes: 4.2 – Ethernet and Internet Protocol (IP)
4.2.5 – The Default Gateway
4.2.5.3 – Using the Default Gateway

## Slide 34: IPv6 Need for IPv6
The depletion of IPv4 address space has been the motivating factor for moving to IPv6.128-bit address space.
Four out of the five Regional Internet Registries (RIRs) have run out of IPv4 addresses.
Notes: 4.2 – Ethernet and Internet Protocol (IP)
4.2.6 – IPv6
4.2.6.1 – Need for IPv6

## Slide 35: IPv6 IPv6 Size and Representation
128-bit address space.
  String of 32 hexadecimal values.
  Every 4 bits represented by one hexadecimal digit.
  Hextet is 16 bits or 4 hexadecimal digits.
Notes: 4.2 – Ethernet and Internet Protocol (IP)
4.2.6 – IPv6
4.2.6.2 – IPv6 Size and Representation

## Slide 36: IPv6 IPv6 Address Formatting
IPv6 Addresses:
  128 bit address space.
  Can remove leading zeros.
  Can leave out 1 “all zeros” segment.
  Two sections: Prefix and Interface ID.
Notes: 4.2 – Ethernet and Internet Protocol (IP)
4.2.6 – IPv6
4.2.6.3 – IPv6 Address Formatting

## Slide 37: IPv6 IPv6 Prefix Length
IPv6 Prefix length does not use the dotted decimal subnet mask notation.
The prefix length can range from 0 to 128.
Notes: 4.2 – Ethernet and Internet Protocol (IP)
4.2.6 – IPv6
4.2.6.4 – IPv6 Prefix Length
4.2.6.5- Activity – IPv6 Address Notation

## Slide 38: Connectivity Verification
Notes: 4 – Network Protocols and Services
4.3 – Connectivity Verification

## Slide 39: ICMP ICMPv4 Messages
Used to provide feedback and troubleshoot network problems.
Message types:
  Host confirmation – echo request and echo reply with the ping utility.
  Destination or service unreachable codes:
      0 – net unreachable
      1 – host unreachable
      2 – protocol unreachable
      3 – port unreachable
  Time exceeded – used by a router to indicate that a packet cannot be sent onward:
      IPv4 is due to the time to live (TTL) field having a value of 0.
      IPv6 does not have a TTL field, but has a hop limit field instead.
Notes: 4.3 – Connectivity Verification
4.3.1 - ICMP
4.3.1.1 – ICMPv4 Messages

## Slide 40: ICMP ICMPv6 RS and RA Messages
4 new protocols as part of the Neighbor Discovery Protocol (ND or NDP):
Messaging between IPv6 router and IPv6 device:
  Router Solicitation (RS) – used between an IPv6 device and a router.
  Router Advertisement (RA) – used between an IPv6 router and a device to provide addressing info using Stateless Address Autoconfiguration (SLAAC).
  Messaging between IPv6 devices:
  Neighbor Solicitation (NS) message
  Neighbor Advertisement (NA) message
Notes: 4.3 – Connectivity Verification
4.3.1 - ICMP
4.3.1.2 – ICMPv6 RS and RA Messages

## Slide 41: ICMP ICMPv6 and RA Messages (Cont.)
  IPv6 Duplicate Address Detection (DAD)
      Not required, but recommended.
      If another device on the network has the same global unicast or link-local unicast address, the device will respond with an NA message.
Notes: 4.3 – Connectivity Verification
4.3.1 - ICMP
4.3.1.2 – ICMPv6 RS and RA Messages

## Slide 42: Ping and Traceroute Utilities Ping – Testing and Local Stack
Ping is a testing utility that uses ICMP echo request and echo reply messages to test connectivity between hosts.
To test connectivity to another host on a network, an echo request is sent to the host address using the ping command.
If the host at the specified address receives the echo request, it responds with an echo reply.
Notes: 4.3 – Connectivity Verification
4.3.2 – Ping and Traceroute Utilities
4.3.2.1 – Ping – Testing the Local Stack

## Slide 43: Ping and Traceroute Utilities Ping – Testing Connectivity to Local LAN
You can also use ping to test the ability of a host to communicate on the local network. This is generally done by pinging the IP address of the gateway of the host.
A successful ping to the gateway indicates that the host and the router interface serving as the gateway are both operational on the local network.
For this test, the gateway address is most often used because the router is normally always operational.
Notes: 4.3 – Connectivity Verification
4.3.2 – Ping and Traceroute Utilities
4.3.2.2 – Ping – Testing Connectivity to Local LAN

## Slide 44: Ping and Traceroute Utilities Ping – Testing Connectivity to Remote Host
Ping can also be used to test the ability of a local host to communicate across an internetwork.
Successful ping across the internetwork confirms communication on the local network.
It also confirms the operation of the router serving as the gateway, and the operation of all other routers that might be in the path between the local network and the network of the remote host.
Notes: 4.3 – Connectivity Verification
4.3.2 – Ping and Traceroute Utilities
4.3.2.3 – Ping – Testing Connectivity to Remote Host

## Slide 45: Ping and Traceroute Utilities Traceroute- Testing the Path
Traceroute provides information about the details of devices between the hosts.
Generates a list of hops that were successfully reached along the path:
  Round trip Time (RTT) – time for each hop along path.
  IPv4 TTL and IPv6 Hop Limit - Traceroute makes use of a function of the TTL field in IPv4 and the Hop Limit field in IPv6 in the Layer 3 headers, along with the ICMP time exceeded message.
After the final destination is reached, the host responds with either an ICMP port unreachable message or an ICMP echo reply message instead of the ICMP time exceeded message.
Notes: 4.3 – Connectivity Verification
4.3.2 – Ping and Traceroute Utilities
4.3.2.4 – Traceroute – Testing the Path

## Slide 46: Ping and Traceroute Utilities ICMP Packet Format
ICPM is considered to be a Layer 3 protocol.
ICMP acts as a data payload within the IP packet.
It has a special header data field.
These are some common message codes:
  0 – Echo reply (response to a ping)
  3 – Destination Unreachable
  5 – Redirect (use another route to your destination)
  8 – Echo request (for ping)
  11 – Time Exceeded (TTL became 0)
Notes: 4.3 – Connectivity Verification
4.3.2 – Ping and Traceroute Utilities
4.3.2.5 – ICMP Packet Format

## Slide 47: Address Resolution Protocol
Notes: 4 – Network Protocols and Services
4.4 - Address Resolution Protocol

## Slide 48: MAC and IP Destination on Same Network
Two addresses assigned to an Ethernet device:
  MAC address (Layer 2 physical address)
  IP address (Layer 3 logical address)
A device must have both addresses to communicate with another TCP/IP-based device:
  Uses the source and destination MAC address
  Uses the source and destination IP address
Notes: 4.4 – Address Resolution Protocol
4.4.1 – MAC and IP
4.4.1.1 – Destination on Same Network

## Slide 49: MAC and IP Destination on Remote Network
When communicating with a device on a remote network, the destination MAC address is the MAC address of the Layer 3 device interface on the same network as the device originating the packet.
Notes: 4.4 – Address Resolution Protocol
4.4.1 – MAC and IP
4.4.1.2 – Destination on Remote Network

## Slide 50: ARP Introduction to ARP
When a device sends an Ethernet frame, it contains these two addresses:
  Destination MAC address - The MAC address of the Ethernet NIC, which will be either the MAC address of the final destination device or the router.
  Source MAC address - The MAC address of the sender’s Ethernet NIC.
To determine the destination MAC address, the device uses ARP. ARP resolves IPv4 addresses to MAC addresses, and maintains a table of mappings.
Notes: 4.4 – Address Resolution Protocol
4.4.2 – ARP
4.4.2.1 – Introduction to ARP

## Slide 51: ARP ARP Functions
Used to resolve IPv4 addresses to MAC addresses.
IPv4 and MAC address mappings kept in an ARP table.
Notes: 4.4 – Address Resolution Protocol
4.4.2 – ARP
4.4.2.2 – ARP Functions

## Slide 52: ARP Removing Entries from an ARP Table
For each device, an ARP cache timer removes ARP entries that have not been used for a specified period of time.
Commands may also be used to manually remove all or some of the entries in the ARP table.
Network hosts and routers keep ARP tables.
Notes: 4.4 – Address Resolution Protocol
4.4.2 – ARP
4.4.2.6 – Removing Entries from an ARP Table

## Slide 53: ARP ARP Tables on Networking Devices
Network hosts and routers keep ARP tables.
Held in memory called ARP cache.
Age out and removed from table.
Notes: 4.4 – Address Resolution Protocol
4.4.2 – ARP
4.4.2.7 – ARP Tables on Networking Devices

## Slide 54: ARP Issues ARP Broadcasts
ARP Broadcasts – could impact large networks.
Notes: 4.4 – Address Resolution Protocol
4.4.3 – ARP Issues
4.4.3.1 – ARP Broadcasts

## Slide 55: ARP Issues ARP Spoofing
ARP Spoofing (ARP poisoning) – security risk
  This is a technique used by an attacker to reply to an ARP request for an IPv4 address belonging to another device, such as the default gateway.
Notes: 4.4 – Address Resolution Protocol
4.4.3 – ARP Issues
4.4.3.2 – ARP Spoofing

## Slide 56: The Transport Layer
Notes: 4 – Network Protocols and Services
4.5 – The Transport Layer

## Slide 57: Transport Layer Characteristics Transport Layer Protocol Role in Network Communication
Tracks individual conversations.
Moves data between applications on network devices.
Segments data and reassembles segments.
Identifies applications using a port number.
Notes: 4.5 – The Transport Layer
4.5.1 – Transport Layer Characteristics
4.5.1.1 – Transport Layer Protocol Role in Network communication

## Slide 58: Transport Layer Characteristics Transport Layer Mechanisms
Segmenting the data into smaller chunks enables many different communications, from many different users, to be interleaved (multiplexed) on the same network.
The transport layer is also responsible for managing reliability requirements of a conversation.
TCP/IP provides two transport layer protocols:
  Transmission Control Protocol (TCP)
  User Datagram Protocol (UDP)
Notes: 4.5 – The Transport Layer
4.5.1 – Transport Layer Characteristics
4.5.1.2 – Transport Layer Mechanisms

## Slide 59: TCP/IP Applications
Port Number | Protocol | Application
20 | TCP | FTP data
21 | TCP | FTP control
22 | TCP | SSH
23 | TCP | Telnet
25 | TCP | SMTP
53 | UDP,TCP | DNS
67,68 | UDP | DHCP
69 | UDP | TFTP
80 | TCP | HTTP(WWW)
110 | TCP | POP3
161 | UDP | SNMP
443 | TCP | SSL
16,384–32,767 | UDP | RTP-based Voice(VoIP) and Video

## Slide 60: Transport Layer Characteristics TCP Local and Remote Ports
TCP and UDP manage these multiple simultaneous conversations by using header fields that can uniquely identify these applications. These unique identifiers are the port numbers:
  The source port number is associated with the originating application on the local host.
  The destination port number is associated with the destination application on the remote host.
Notes: 4.5 – The Transport Layer
4.5.1 – Transport Layer Characteristics
4.5.1.3 – TCP Local and Remote Ports

## Slide 61: Transport Layer Characteristics Socket Pairs
The combination of the source IP address and source port number, or the destination IP address and destination port number is known as a socket.
The socket is used to identify the server and service being requested by the client.
Sockets enable multiple processes, running on a client, to distinguish themselves from each other, and multiple connections to a server process to be distinguished from each other.
Notes: 4.5 – The Transport Layer
4.5.1 – Transport Layer Characteristics
4.5.1.4 – Socket Pairs

## Slide 62: Transport Layer Characteristics TCP versus UDP
TCP
  Used for majority of the major TCP/IP protocols.
  Reliable, acknowledges data, resends lost data, delivers data in sequenced order.
      Examples: email, HTTP
UDP
  Fast, low overhead, does not require acknowledgments, does not resend lost data, delivers data as it arrives.
      Examples: VoIP, streaming live videos
Notes: 4.5 – The Transport Layer
4.5.1 – Transport Layer Characteristics
4.5.1.5 – TCP vs. UDP

## Slide 63: Transport Layer Characteristics TCP and UDP Headers
TCP
  TCP is a stateful protocol. A stateful protocol is a protocol that keeps track of the state of the communication session.
  To track the state of a session, TCP records which information it has sent and which information has been acknowledged.
  The stateful session begins with the session establishment and ends when closed with the session termination.
UDP
  UDP is a stateless protocol, meaning neither the client, nor the server, is obligated to keep track of the state of the communication session.
  If reliability is required when using UDP as the transport protocol, it must be handled by the application.
UDP Datagram
TCP Segment
Notes: 4.5 – The Transport Layer
4.5.1 – Transport Layer Characteristics
4.5.1.6 – TCP and UDP Headers
4.5.1.7 – Activity TCP and UDP Characteristics

## Slide 64: Transport Layer Operation TCP Port Allocation
Destination port numbers:
  Uses well-known port numbers.
Source port numbers:
  Uses dynamic port numbers.
  When establishing a connection with a server, the transport layer on the client establishes a source port to keep track of data sent from the server.
  Just as a server can have many ports open for server processes, clients can have many ports open for connections to multiple sockets.
Notes: 4.5 – The Transport Layer
4.5.2 – Transport Layer Operation
4.5.2.1 – TCP Port Allocation

## Slide 65: TCP and UDP Vulnerabilities TCP
TCP segment information appears immediately after the IP header.
TCP provides the following services:
  Reliable delivery
  Flow control
  Stateful communication
Notes: 7.2 – Attacking the Foundation
7.2.2 – TCP and UDP Vulnerabilities
7.2.2.1 – TCP

## Slide 66: Transport Layer Operation A TCP Session Part 1: Connection Establishment and Termination
A TCP connection is established in three steps:
  The initiating client requests a client-to-server communication session with the server.
  The server acknowledges the client-to-server communication session and requests a server-to-client communication session.
  The initiating client acknowledges the server-to-client communication session.
Notes: 4.5 – The Transport Layer
4.5.2 – Transport Layer Operation
4.5.2.2 – A TCP Session Part 1: Connection Establishment and Termination

## Slide 67: The Transport Layer Operation A TCP Session Part 2: Data Transfer
TCP Order Delivery:
  Segment sequence numbers indicate how to reassemble and reorder received segments.
  The receiving TCP process places the data into a receiving buffer.
  Out of order segments are held for later processing.
  When the segments with the missing bytes arrive, these segments are processed in order.
Flow Control:
  Controls the amount of data that the destination can receive and process reliably by adjusting the rate of data flow.
Notes: 4.5 – The Transport Layer
4.5.2 – Transport Layer Operation
4.5.2.6 – A TCP Session Part II: Data Transfer

## Slide 68: The Transport Layer Operation UDP Session
UDP Session:
  Resembles the data in the order it was received.
  Assigned well-known or registered port numbers.
Notes: 4.5 – The Transport Layer
4.5.2 – Transport Layer Operation
4.5.2.9 – UDP Session

## Slide 69: Network Services
Notes: 4 – Network Protocols and Services
4.6 – Network Services

## Slide 70: DHCP DHCP Overview
Dynamic Host Configuration Protocol (DHCP)
  Provides IP addressing information such as IP address, subnet mask, default gateway, DNS server IP address and domain name.
  Messages
    Discover
    Offer
    Request
    Ack(nowledge)
Notes: 4.6 – Network Services
4.6.1 - DHCP
4.6.1.1 – DHCP Overview

## Slide 71: DHCP DHCPv4 Message Format
A DHCP message contains the following fields:
Operation (OP) Code - Specifies the general type of message.
Hardware Type - Identifies the type of hardware used in the network.
Hardware Address Length - Specifies the length of the address.
Hops - Controls the forwarding of messages.
Transaction Identifier - Used by the client to match the request with replies received from DHCPv4 servers.
Seconds - Identifies the number of seconds elapsed since a client began attempting to acquire or renew a lease.
Flags - Used by a client that does not know its IPv4 address when it sends a request.
Notes: 4.6 – Network Services
4.6.1 - DHCP
4.6.1.2 – DHCPv4 Message Format

## Slide 72: DHCP DHCPv4 Message Format (Cont.)
A DHCP message contains the following fields:
Client IP Address - Used by a client during lease renewal when the address of the client is valid and usable, not during the process of acquiring an address.
Your IP Address - Used by the server to assign an IPv4 address to the client.
Server IP Address - Used by the server to identify the address of the server that the client should use for the next step in the bootstrap process.
Gateway IP Address - Routes DHCPv4 messages when DHCPv4 relay agents are involved.
Client Hardware Address - Specifies the physical layer of the client.
Server Name - Used by the server sending a DHCPOFFER or DHCPACK message.
Boot Filename - Optionally used by a client to request a particular type of boot file in a DHCPDISCOVER message.
DHCP Options - Holds DHCP options, including several parameters required for basic DHCP operation.
Notes: 4.6 – Network Services
4.6.1 - DHCP
4.6.1.2 – DHCPv4 Message Format

## Slide 73: DNS DNS Overview
Dynamic Name System (DNS)
  Manages and provides domain names and associated IP addresses.
  Hierarchy of servers.
  90% of malicious software used to attack networks uses DNS to carry out attack campaigns.
Notes: 4.6 – Network Services
4.6.2 – DNS
4.6.2.1 – DNS Overview

## Slide 74: DNS DNS Domain Hierarchy
Dynamic Name System (DNS)
    The DNS consists of a hierarchy of generic top level domains (gTLD) which consist of .com, .net, .org, .gov, .edu, and numerous country-level domains, such as .br (Brazil), .es (Spain),.uk (United Kingdom).
    Second-level domains are represented by a domain name that is followed by a top-level domain.
    Subdomains are found at the next level of the DNS hierarchy and represent some division of the second-level domain.
    Finally, a fourth level can represent a host in a subdomain.
Notes: 4.6 – Network Services
4.6.2 – DNS
4.6.2.2 – The DNS Domain Hierarchy

## Slide 75: DNS DNS Lookup Process
To understand DNS, cybersecurity analysts should be familiar with the following terms:
Resolver - A DNS client that sends DNS messages to obtain information about the requested domain name space.
Recursion - The action taken when a DNS server is asked to query on behalf of a DNS resolver.
Authoritative Server - A DNS server that responds to query messages with information stored in Resource Records (RRs) for a domain name space stored on the server.
Recursive Resolver - A DNS server that recursively queries for the information asked in the DNS query.
Notes: 4.6 – Network Services
4.6.2 – DNS
4.6.2.3 – DNS Lookup Process

## Slide 76: DNS DNS Lookup Process (Cont.)
To understand DNS, cybersecurity analysts should be familiar with the following terms:
FQDN - A Fully Qualified Domain Name is the absolute name of a device within the distributed DNS database.
RR - A Resource Record is a format used in DNS messages that is composed of the following fields: NAME, TYPE, CLASS, TTL, RDLENGTH, and RDATA.
Zone - A database that contains information about the domain name space stored on an authoritative server.
.
Notes: 4.6 – Network Services
4.6.2 – DNS
4.6.2.3 – DNS Lookup Process

## Slide 77: DNS DNS Message Format
DNS uses UDP port 53 for DNS queries and responses.
DNS queries originate at a client and responses are issued from DNS servers.
If a DNS response exceeds 512 bytes such as when Dynamic DNS (DDNS) is used, TCP port 53 is used to handle the message.
DNS Record Types:
  A - An end device IPv4 address
  NS - An authoritative name server
  AAAA - An end device IPv6 address
  MX - A mail exchange record
Notes: 4.6 – Network Services
4.6.2 – DNS
4.6.2.4 – DNS Message Format

## Slide 78: DNS Dynamic DNS
Dynamic DNS (DDNS)
  Allows a user or organization to register an IP address with a domain name as in DNS.
  When the IP address of the mapping changes, the new mapping can be propagated through the DNS almost instantaneously.
Notes: 4.6 – Network Services
4.6.2 – DNS
4.6.2.5 – Dynamic DNS

## Slide 79: DNS The WHOIS Protocol
WHOIS Protocol:
  WHOIS is a TCP-based protocol that is used to identify the owners of Internet domains through the DNS system.
Notes: 4.6 – Network Services
4.6.2 – DNS
4.6.2.6. WHOIS Protocol

## Slide 80: NAT NAT – Overview
Network Address Translation (NAT)
  Not enough public IPv4 addresses to assign a unique address to each device connected to the Internet.
  Private IPv4 addresses are used within an organization or site to allow devices to communicate locally.
  Private IPv4 addresses cannot be routed over the Internet.
  Used on border devices.
Notes: 4.6 – Network Services
4.6.3 - NAT
4.6.3.1 – NAT- Overview

## Slide 81: NAT NAT – Enabled Routers
Network Address Translation (NAT)
  When an internal device sends traffic out of the network, the NAT-enabled router translates the internal IPv4 address of the device to a public address from the NAT pool.
  To outside devices, all traffic entering and exiting the network appears to have a public IPv4 address from the provided pool of addresses.
  A NAT router typically operates at the border of a stub network.
Notes: 4.6 – Network Services
4.6.3 - NAT
4.6.3.2 – NAT Enabled Routers

## Slide 82: NAT Port Address Translation
Port Address Translation (PAT)
  One-to-many – Many internal address translations to one or more public IP addresses
Notes: 4.6 – Network Services
4.6.3 - NAT
4.6.3.3 – PAT Port Address Translation

## Slide 83: File Transfer and Sharing Services FTP and TFTP
File Transfer Protocol (FTP)
  TCP-based.
  Used to push and pull data from a server.
Trivial File Transfer Protocol (TFTP)
  UDP-based.
  Fast, but unreliable.
Server Message Block (SMB)
  Client/server-based file sharing protocol.
Notes: 4.6 – Network Services
4.6.4 – File Transfer and Sharing Services
4.6.4.1 – FTP and TFTP

## Slide 84: File Transfer and Sharing Services SMB
Server Message Block (SMB)
  Client/server-based file sharing protocol.
  This format uses a fixed-sized header, followed by a variable-sized parameter and data component.
  SMB messages can start, authenticate, and terminate sessions, control file and printer access, and allow an application to send or receive messages to or from another device.
Notes: 4.6 – Network Services
4.6.4 – File Transfer and Sharing Services
4.6.4.2 -SMB

## Slide 85: Email Email Overview
Email supports three separate protocols for operation:
  Simple Mail Transfer Protocol (SMTP)
  Post Office Protocol version 3 (POP3)
  IMAP
  The application layer process that sends mail uses SMTP. A client retrieves email using one of the two application layer protocols: POP3 or IMAP.
Notes: 4.6 – Network Services
4.6.5 - Email
4.6.5.1 – Email Overview

## Slide 86: Email SMTP
SMTP
  Simple Mail Transfer Protocol (SMTP) – Port 25.
After the connection is made, the client attempts to send the email to the server across the connection.
When the server receives the message, it either places the message in a local account, if the recipient is local, or forwards the message to another mail server for delivery.
Notes: 4.6 – Network Services
4.6.5 - Email
4.6.5.2 – SMTP

## Slide 87: Email POP3
With POP3, mail is downloaded from the server to the client and then deleted on the server.
With POP3, email messages are downloaded to the client and removed from the server, so there is no centralized location where email messages are kept.
Notes: 4.6 – Network Services
4.6.5 - Email
4.6.5.3 – POP3

## Slide 88: Email IMAP
When a user connects to an IMAP-capable server, copies of the messages are downloaded to the client application.
When a user decides to delete a message, the server synchronizes that action and deletes the message from the server.
Notes: 4.6 – Network Services
4.6.5 - Email
4.6.5.4 – IMAP

## Slide 89: HTTP HTTP Overview
Hypertext Transfer Protocol (HTTP) :
  Port 80
  Governs the way a web server and client interact.
  TCP-based
  Has specific server responses.
Steps:
  Client initiates HTTP request to server.
  HTTP returns code for a webpage.
  Browser interprets HTML code and displays on webpage.
Notes: 4.6 – Network Services
4.6.6 – HTTP
4.6.6.1 – HTTP Overview

## Slide 90: HTTP The HTTP URL
HTTP URLs can also specify the port on the server that should handle the HTTP methods.
In addition, it can specify a query string and fragment.
Query string typically contains information that is not handled by the HTTP server process itself, but is instead handled by another process that is running on the server.
Notes: 4.6 – Network Services
4.6.6 – HTTP
4.6.6.2 – The HTTP URL

## Slide 91: Network Services The HTTP Protocol
HTTP is a request/response protocol that uses TCP port 80.
When a client, typically a web browser, sends a request to a web server, it will use one of six methods that are specified by the HTTP protocol.
  GET - A client request for data. A client (web browser) sends the GET message to the web server to request HTML pages.
  POST - Submits data to be processed by a resource.
  PUT - Uploads resources or content to the web server.
  DELETE - Deletes the resource specified.
  OPTIONS - Returns the HTTP methods that the server supports.
  CONNECT - Requests that an HTTP proxy server forwards the HTTP TCP session to the desired destination.
Notes: 4.6 – Network Services
4.6.6 – HTTP
4.6.6.3 – The HTTP Protocol

## Slide 92: HTTP HTTP Status Code
The HTTP server responses are identified with various status codes that inform the host application of the outcome of client requests to the server. The codes are organized into five groups.
  1xx - Informational
  2xx - Success
  3xx - Redirection
  4xx - Client Error
  5xx - Server Error
Notes: 4.6 – Network Services
4.6.6 – HTTP
4.6.6.4 – HTTP Status Code